## Slide 1: Lab 1A - Sequence Generator

## Slide 2: Sequence generator
A sequence generator is a sequential circuit which generates a prescribed sequence at its output in synchronization through a CLK.
The length of the series may be indefinite otherwise fixed.
A sequence generator can be used as a code generator, counters, random bit generators, sequence, and prescribed period generator.
A simple sequence generator can be designed by MUX and Flip Flops (FFs).
MUX is a combinational logic circuit designed to combine several input signals and sent them to a single out by selecting lines.
A FF is an electronic component consisting of two stable states and is used to store state information.

## Slide 3: Implementation LAB 1A
Deliverables:
Sequence generator:
Design and implement a sequence generator to generate a sequence which has a 10 or more different states: 0, 11, 14, 5, 4, 15, 12, 9, 2,13, 0, 11, ...
Ensure that all invalid stages of the machine clear it (set it too state zero.)
Make sure you have 0 and 15 in your sequence.

## Slide 4: Sequence generator
PS | D MSB | C | B | A LSB | NS | D+ | C+ | B+ | A+
0 | 0 | 0 | 0 | 0 | 11 | 1 | 0 | 1 | 1
1 | 0 | 0 | 0 | 1 |  | 0 | 0 | 0 | 0
2 | 0 | 0 | 1 | 0 | 13 | 1 | 1 | 0 | 1
3 | 0 | 0 | 1 | 1 |  | 0 | 0 | 0 | 0
4 | 0 | 1 | 0 | 0 | 15 | 1 | 1 | 1 | 1
5 | 0 | 1 | 0 | 1 | 4 | 0 | 1 | 0 | 0
6 | 0 | 1 | 1 | 0 |  | 0 | 0 | 0 | 0
7 | 0 | 1 | 1 | 1 |  | 0 | 0 | 0 | 0
8 | 1 | 0 | 0 | 0 |  | 0 | 0 | 0 | 0
9 | 1 | 0 | 0 | 1 | 2 | 0 | 0 | 1 | 0
10 | 1 | 0 | 1 | 0 |  | 0 | 0 | 0 | 0
11 | 1 | 0 | 1 | 1 | 14 | 1 | 1 | 1 | 0
12 | 1 | 1 | 0 | 0 | 9 | 1 | 0 | 0 | 1
13 | 1 | 1 | 0 | 1 | 0 | 0 | 0 | 0 | 0
14 | 1 | 1 | 1 | 0 | 5 | 0 | 1 | 0 | 1
15 | 1 | 1 | 1 | 1 | 12 | 1 | 1 | 0 | 0
The sequence : 0, 11, 14, 5, 4, 15, 12, 9, 2,13,
0, 11, ...
0000
1011
1110
1101
Design using D flip-flop and MUX.

## Slide 5: MUX Design
PS | D MSB | C | B | A LSB | NS | D+ | C+ | B+ | A+
0 | 0 | 0 | 0 | 0 | 11 | 1 | 0 | 1 | 1
1 | 0 | 0 | 0 | 1 |  | 0 | 0 | 0 | 0
2 | 0 | 0 | 1 | 0 | 13 | 1 | 1 | 0 | 1
3 | 0 | 0 | 1 | 1 |  | 0 | 0 | 0 | 0
4 | 0 | 1 | 0 | 0 | 15 | 1 | 1 | 1 | 1
5 | 0 | 1 | 0 | 1 | 4 | 0 | 1 | 0 | 0
6 | 0 | 1 | 1 | 0 |  | 0 | 0 | 0 | 0
7 | 0 | 1 | 1 | 1 |  | 0 | 0 | 0 | 0
8 | 1 | 0 | 0 | 0 |  | 0 | 0 | 0 | 0
9 | 1 | 0 | 0 | 1 | 2 | 0 | 0 | 1 | 0
10 | 1 | 0 | 1 | 0 |  | 0 | 0 | 0 | 0
11 | 1 | 0 | 1 | 1 | 14 | 1 | 1 | 1 | 0
12 | 1 | 1 | 0 | 0 | 9 | 1 | 0 | 0 | 1
13 | 1 | 1 | 0 | 1 | 0 | 0 | 0 | 0 | 0
14 | 1 | 1 | 1 | 0 | 5 | 0 | 1 | 0 | 1
15 | 1 | 1 | 1 | 1 | 12 | 1 | 1 | 0 | 0
4 D- Flip Flops
Use Mux to derive the input of each flip flops.
Use CBA as the select for MUX
0
1
000 001 010 011 100 101 110 111
CBA
D
1
0
0
0
1
0
0
0
1 0 0 0
1 0 1 0
8:1
D0 D1 D2 D3 D4 D5 D6 D7
8:1
3 selected lines
23 Inputs

## Slide 6: Circuit Diagram
0
1
000 001 010 011 100 101 110 111
CBA
D
1
0
0
0
1
0
0
0
1 0 0 0
1 0 1 0
A-FF
LSB
B-FF
C-FF
D-FF
MSB
8:1

## Slide 7
A-FF
LSB
B-FF
C-FF
D-FF
MSB
8:1
+
-
R
R
R
R
GND
8:1
8:1
8:1

## Slide 8: Circuit Implementation
You need
  4 FFs – 2 x 7474 (Each 7474 has two FFs)
    A-FF, B-FF, C-FF and D-FF
  4 Muxs – 4 x 74151
    Mux A, Mux B , Mux C, Mux D

## Slide 9: ICs
7474 Dual Positive Edge Triggered D-FF
  Vcc to PR and CLR Pin
74151 8:1 Mux.
  Gnd to Strobe Pin
74151

## Slide 10: Circuit Implementation Tutorial
74151
7474
D3 VCC
D2 D4
D1 D5
D0 D6
Y D7
W A
S B
GND C
S B
1CLR VCC
1CK 2D
1PR 2CK
1Q 2PR
1Q‘ 2Q
Vcc 2Q’
1D 2CLR
7474
1CLR VCC
1CK 2D
1PR 2CK
1Q 2PR
1Q‘ 2Q
Vcc 2Q’
1D 2CLR
7474

## Slide 11: Circuit Implementation Tutorial
7474:
CLR: Active High
PRE: Active High
Connect them to VCC
74151:
Strode: Active Low
Connect it to GND

## Slide 12: Circuit Implementation Tutorial

## Slide 13: Circuit Implementation Tutorial

## Slide 14: Terrible Circuit
Impossible to follow any of the connections
No color coding
Thick wads of wire
Takes forever to debug (this is my circuit from this class)

## Slide 15: Great Circuit
Minimally length wires
Minimal crossover wires makes it easier to follow connections
Color coded different regions
No crossovers above an IC, makes it possible to remove broken ones

## Slide 16: Extra Credit
Modify your sequence detector circuit such that any state, your circuit can go to 0. (10 points)

## Slide 17: 7 Segment Display
Two 7 segment displays on Training Board.
Each has built-in BCD Conversion Circuit.(A is LSB and D is MSB).
 | D | C | B | A | a | b | c | d | e | f | g
0 | 0 | 0 | 0 | 0 | 1 | 1 | 1 | 1 | 1 | 1 | 0
1 | 0 | 0 | 0 | 1 | 0 | 1 | 1 | 0 | 0 | 0 | 0
2 | 0 | 0 | 1 | 0 | 1 | 1 | 0 | 1 | 1 | 0 | 1
3 | 0 | 0 | 1 | 1 | 1 | 1 | 1 | 1 | 0 | 0 | 1
4 | 0 | 1 | 0 | 0 | 0 | 1 | 1 | 0 | 0 | 1 | 1
5 | 0 | 1 | 0 | 1 | 1 | 0 | 1 | 1 | 0 | 1 | 1
6 | 0 | 1 | 1 | 0 | 0 | 0 | 1 | 1 | 1 | 1 | 1
7 | 0 | 1 | 1 | 1 | 1 | 1 | 1 | 0 | 0 | 0 | 0
8 | 1 | 0 | 0 | 0 | 1 | 1 | 1 | 1 | 1 | 1 | 1
9 | 1 | 0 | 0 | 1 | 1 | 1 | 1 | 0 | 0 | 1 | 1

## Slide 18: Display the Sequence
A
B
C
D
A
B
C
D
D C B A |  |  |  | D C B A |  |  | 
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 0 | 0 | 0 | 1 | 0
0 | 0 | 0 | 0 | 0 | 1 | 0 | 0
0 | 0 | 0 | 0 | 0 | 1 | 0 | 1
0 | 0 | 0 | 0 | 1 | 0 | 0 | 1
0 | 0 | 0 | 1 |  |  |  | 
0 | 0 | 0 | 1 |  |  |  | 
0 | 0 | 0 | 1 |  |  |  | 
0 | 0 | 0 | 1 |  |  |  | 
0 | 0 | 0 | 1 |  |  |  | 
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 0 | 0 | 0 | 1 | 0
0 | 0 | 0 | 0 | 0 | 1 | 0 | 0
0 | 0 | 0 | 0 | 0 | 1 | 0 | 1
0 | 0 | 0 | 0 | 1 | 0 | 0 | 1
0 | 0 | 0 | 1 |  |  |  | 
0 | 0 | 0 | 1 |  |  |  | 
0 | 0 | 0 | 1 |  |  |  | 
0 | 0 | 0 | 1 |  |  |  | 
0 | 0 | 0 | 1 |  |  |  | 
PS | D MSB | C | B | A LSB
0 | 0 | 0 | 0 | 0
2 | 0 | 0 | 1 | 0
4 | 0 | 1 | 0 | 0
5 | 0 | 1 | 0 | 1
9 | 1 | 0 | 0 | 1
11 | 1 | 0 | 1 | 1
12 | 1 | 1 | 0 | 0
13 | 1 | 1 | 0 | 1
14 | 1 | 1 | 1 | 0
15 | 1 | 1 | 1 | 1

## Slide 19
A-FF
LSB
B-FF
C-FF
D-FF
MSB
8:1
Sequence Generator
A
B
C
D
A
B
C
D
Combination Logic For Display
Display Circuit