## Slide 1: LAB-3. 4 Bit Adder- 4 Bit Subtractor
Deliverables:
Implement a 4 bit Adder
    Implement a one bit full adder with carry in and carry out pin using Quartus prime Schematic Block.
    Connect 4 one-bit full adder in series to get a 4-bit full adder.
  Modify the 4 bit adder to do subtraction.
    Use the 2nd complement system to represent negative number and perform addition.
    Eg.
Compilation and Simulation on Quartus Prime.
Implement a 4 bit Adder/Subtractor.
Implement a display ckt which displays a negative binary number into a negative decimal number.
  Eg. + 5 -5
Implement a fully functional 4 bit Adder/Subtractor with display circuit and BCD from Lab 3 and test it
on DE1 Board.
LAB 4
LAB 3

## Slide 2: Binary Addition
Binary 1 bit addition
  0 + 0 = 0
  1 + 0 = 1
  0 + 1 = 1
  1 + 1 = 0 with carry out of 1.
When implement adder using logic gates, we need to add the carry input (from the previous bit) and carry out output.
Eg.
1 1 0 1
+ 1 1 1 0
1
0
1
0
0
1
1
1

## Slide 3: Binary Addition
Binary 1 bit addition
  0 + 0 = 0
  1 + 0 = 1
  0 + 1 = 1
  1 + 1 = 0 with carry out of 1.
When implement adder using logic gates, we need to add the carry input (from the previous bit) and carry out output.
Eg.
1 1 0 1
+ 1 1 1 0
1
0
1
0
0
1
1
1
Carry Out
Carry Out
Carry In
Carry out
Carry In
Carry out
Carry In

## Slide 4: 1 Bit Full Adder
X | Y | Cin | Sum | Cout
0 | 0 | 0 | 0 | 0
0 | 0 | 1 | 1 | 0
0 | 1 | 0 | 1 | 0
0 | 1 | 1 | 0 | 1
1 | 0 | 0 | .. | ..
1 | 0 | 1 | .. | ..
1 | 1 | 0 | .. | ..
1 | 1 | 1 | .. | ..
1 bit adder
Sum
Cout
Cin
Y
X
????

## Slide 5: 4 Bit Adder
4 bit adder
1 Bit Adder
Sum
Cout0
Cin
Y
X
1 Bit Adder
Sum
Cout1
Cin1
Y
X
1 Bit Adder
Sum
Cout2
Cin2
Y
X
1 Bit Adder
Sum
Cout
Cin3
Y
X
Four 1 bit adders in series to get a 4 bit adder.
Block diagram of a 4 bit adder .
A3 A2 A1 A0
+ B3 B2 B1 B0
Q0
Cin1
Q1
Cin2
Q2
Cin3
Q3
Cout
Cin
Cout0
Cout1
Cout2

## Slide 6: 2nd Complement
Binary representation of a negative number.
Eg.
In the 2nd complement system, MSB is used as a sign bit.
  MSB = 0 represents the binary number is a positive integer.
  MSB = 1 represents the binary number is a negative integer.
Binary Bit can represent positive integer and negative integer.
  Eg. 4 bit binary number can represent up to (0-7) and (-1 to -8)
-

## Slide 7: Example of Negative Number Representation for 4 bit system in 2nd Complement
Binary |  |  |  | Integer
0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 1 | 1
0 | 0 | 1 | 0 | 2
0 | 0 | 1 | 1 | 3
0 | 1 | 0 | 0 | 4
0 | 1 | 0 | 1 | 5
0 | 1 | 1 | 0 | 6
0 | 1 | 1 | 1 | 7
1 | 0 | 0 | 0 | -8
1 | 0 | 0 | 1 | -7
1 | 0 | 1 | 0 | -6
1 | 0 | 1 | 1 | -5
1 | 1 | 0 | 0 | -4
1 | 1 | 0 | 1 | -3
1 | 1 | 1 | 0 | -2
1 | 1 | 1 | 1 | -1

## Slide 8: 4 Bit Subtractor
4 Bit Add/
Subtractor
Sign Bit

## Slide 9: 4 Bit Subtractor
X Y
Design a subtractor such that X-Y = X + (-Y)
The max integer we can input from Y is 15, 1111.
To represent (-15) in binary we need a 5 bit binary system.
Eg.
This is wrong!!!!
-15 in Binary..
In a 4 bit system, add one MSB bit for Sign Bit
Sign Bit

## Slide 10: 4 Bit Adder/Subtractor
Eg. X = 9, Y =14 : X-Y
Find the 2nd complement of .
which is .
Add (00001) and then add to
get the final answer.
-14
-5
Sign bit tells the result is a negative number.

## Slide 11: Sign Bit
Sign bit = 0+1+ carry out from (X3+Y3’).
= 1+carry out from (X3+Y3’).
-14
-5
Carry Out from (A3+B3’) | Sign Bit
1 | 0
0 | 1
Therefore, from the truth table above, Sign Bit = Not Carry out from (A3+B3’).

## Slide 12: 4 Bit Subtractor
4 bit adder
Block diagram of a 4 bit subtractor using 4 bit adder .
1 Bit Adder
Sum
Cout0
Cin
Y
X
1 Bit Adder
Sum
Cout1
Cin1
Y
X
1 Bit Adder
Sum
Cout2
Cin2
Y
X
1 Bit Adder
Sum
Cout
Cin3
Y
X

## Slide 13: Try to design 4 Bit Adder/Subtractor
Modify the 4-bit Adder to a 4-bit Adder/Subtractor.
Use four 2:1 Muxs and 4-bit adder to implement 4-bit Adder/Subtractor.

## Slide 14: Project Flow Chart
Implement a 1-bit Adder.
Simulate 1 1-bit adder (Screenshot the result and add it to the report).
Implement a 4-bit Adder.
Simulation waveform on Quartus Prime (Screenshot the result and add it in the report.)
Modify the 4-bit Adder to a 4-bit Sub.
Simulation waveform on Quartus Prime. (Screenshot the result and add it to the report.)

## Slide 15: Report
Follow the sample report for details.
  Objective (10 points)
  Equipment (10 points)
  Description(10 points)
  Design Synthesis (20 points)
    Kmaps and Boolean Expressions
  Complete logic Diagram from Quartus(20 points)
    Screenshot of your Complete Circuit block diagram
  Results and Simulation (10 points)
      Simulation Screenshot with a clear explanation.
        Screenshots for 1-bit adder, 4 bit adder, 4 bit sub/add.
  Conclusion (20 points).