## Slide 1: LAB 4 – BCD and Seven Segment Display
To design a BCD and 7-segment Display Using QuarTUS Prime Software.

## Slide 2: Implementation
Deliverables:.
Design a circuit to decode a 8 bit binary to BCD and combine with a display circuit from Lab 2.
Simulate the BCD circuit.

## Slide 3: BCD
A BCD is a binary system which represents one decimal number with 4 binary number.
  15  1111 (in Binary)
  15 0001 0101 (in BCD)
Implement a ckt that convert a 8 bit binary input to two BCD.
Maximum binary the ckt can decode is 99.
When the input is higher than 99, overflow = ‘1’.

## Slide 4: BCD: Binary Coded Decimal
Decimal | Binary Number | BCD Outputs | OverFlow
0 1 . . . | 0000 0000 0000 0001 . . . | 0000 0000 0000 0001 | 0 . . .
9 | 0000 1001 | 0000 1001 | 0
10 | 0000 1010 | 0001 0000 | 0
11 | 0000 1011 | 0001 0001 | 0
12 | 0000 1100 | 0001 0010 | 0
. . . 99 | . . . 0110 0011 | 1001 1001 | . . . 0
100 | 0110 0100 | xxxx xxxx | 1

## Slide 5: Binary to BCD
To convert the binary 1111 to BCD, simply add 0110 (6) to 1111.
1111 + 0110 = 1 0101
How about decimal 34?
10 0010 + 0110 = 10 1000
0001 0101
2 8
34
0010 1000
BCD value incorrect..

## Slide 6: Shift Add 3 Alg
Do 8 times ( for 8 bit binary input).
  1. Shift left one to the binary input.
  2. Add 3 to BCD if it’s greater than 4.
  3. Go to 1.

## Slide 7: Shift Add 3 Alg
Eg. Convert 34 to BCD using Shift Add 3 Alg.
  34 = 10 0010
Start output = 0000 0000 (Since we went to convert the input two BCDs.)
Take the first 3 MSB of inputs and add to output.
  Output = 0000 0100
Check whether output is greater than 4. If so add 3 to output.
Shift left one.
  Output = 0000 1000
If output is greater than 4 add 3.
  Output = 0000 1000 + 0000 0011 = 0000 1011
Shift left one.
  Output = 0001 0111
If output is greater than 4 add 3.
  Output = 0001 0111 + 0000 0011 = 0001 1010
Shift left one.
  Output = 0011 0100
3
4

## Slide 8: Shift Add 3 Alg
Input = HGFE DCBA
Take the first 3 MSB of inputs and add to output.
  Output = 0000 0HGF
If 00HGF > 4
  I H1 G1 F1 = 0 H G F + 0011.
Else
  I H1G1F1 = 0 H G F
Shift left one.
  Output = 000I H1 G1 F1 E
If H1 G1 F1 E > 4
  H2 G2 F2 E1 = H1 G1 F1 E + 0011.
Else
  H2 G2 F2 E1 = H1 G1 F1 E
Shift left one.
  Output = 00I H2 G2 F2 E1 D
If G2 F2 E1 D > 4
  G3 F3 E2 D1 = G2 F2 E1 D + 0011.
Else
  G3 F3 E2 D1 = G2 F2 E1 D
Shift left one.
  Output = 0I H2 G3 F3 E2 D1 C
If 0I H2 G3 > 4
  J I1 H3 G4 = 0 I H2 G3 + 0011.
Else
  J I1 H3 G4 = 0 I H2 G3
  If F3 E2 D1 C > 4
  F4 E3 D2 C1 = F3 E2 D1 C + 0011.
Else
  F4 E3 D2 C1 = F3 E2 D1 C
Shift left one.
  Output = I1 H3 G4 F4 E3 D2 C1 B
If I1 H3 G4 F4 > 4
  I2 H4 G5 F5 = I1 H3 G4 F4 + 0011.
Else
  I2 H4 G5 F5 = I1 H3 G4 F4
If E3 D2 C1 B > 4
  E4 D3 C2 B1 = E3 D2 C1 B+ 0011.
Else
  E4 D3 C2 B1 = E3 D2 C1 B
Shift left one.
  Output= H4 G5 F5 E4 D2 C2 B1 A

## Slide 9: Add 3 Ckt
Input X3X2X1X0 | Output P3P2P1P0
0000 0001 0010 0011 0100 0101 0110 0111 1000 1001 | 0000 0001 0010 0011 0100 1000 1001
1010 . . 1111 | xxxx . . xxxx
If Input 4
Output = Input +3;
Else
Output = Input;
End
When .
Input = 0101 (which is greater than 4)
Output = 0101 + 0011 = 1000
Fill these outputs
When input > 9, don’t care.

## Slide 10: Add 3 Ckt
Complete the Truth Table from prev slide
Find the Boolean expression for P3, P2, P1 and P0.
Implement the Ckt .
Simulate the ckt (screen shots for report.)
Create a block symbol (bsf) file for Add-3 ckt. Creating a symbol block
Add -3
Ckt
X3
X2
X1
X0
P3
P2
P1
P0

## Slide 11
If 0HGF > 4
  I H1 G1 F1 = 0 H G F + 0011.
Else
  I H1G1F1 = 0 H G F
Shift left one.
  Output = 000I H1 G1 F1 E
If H1 G1 F1 E > 4
  H2 G2 F2 E1 = H1 G1 F1 E + 0011.
Else
  H2 G2 F2 E1 = H1 G1 F1 E
Shift left one.
  Output = 00I H2 G2 F2 E1 D
If G2 F2 E1 D > 4
  G3 F3 E2 D1 = G2 F2 E1 D + 0011.
Else
  G3 F3 E2 D1 = G2 F2 E1 D
Shift left one.
  Output = 0I H2 G3 F3 E2 D1 C
If 0I H2 G3 > 4
  J I1 H3 G4 = 0 I H2 G3 + 0011.
Else
  J I1 H3 G4 = 0 I H2 G3
  If F3 E2 D1 C > 4
  F4 E3 D2 C1 = F3 E2 D1 C + 0011.
Else
  F4 E3 D2 C1 = F3 E2 D1 C
Shift left one.
  Output = I1 H3 G4 F4 E3 D2 C1 B
If I1 H3 G4 F4 > 4
  I2 H4 G5 F5 = I1 H3 G4 F4 + 0011.
Else
  I2 H4 G5 F5 = I1 H3 G4 F4
If E3 D2 C1 B > 4
  E4 D3 C2 B1 = E3 D2 C1 B+ 0011.
Else
  E4 D3 C2 B1 = E3 D2 C1 B
Shift left one.
  Output= H4 G5 F5 E4 D2 C2 B1 A
Let’s the final output of BCD = U3U2U1U0 L3L2L1L0
Add-3
Ckt
X3
X2
X1
X0
P3
P2
P1
P0
0
H
G
F
I
H1
G1
F1
Add-3
Ckt
X3
X2
X1
X0
P3
P2
P1
P0
H1
G1
F1
E
H2
G2
F2
E1
Add-3
Ckt
X3
X2
X1
X0
P3
P2
P1
P0
G2
F2
E1
D
G3
F3
E2
D1
Add-3
Ckt
X3
X2
X1
X0
P3
P2
P1
P0
0
I
H2
G3
J
I1
H3
G4
Add-3
Ckt
X3
X2
X1
X0
P3
P2
P1
P0
F3
E2
D1
C
F4
E3
D2
C1
Add-3
Ckt
X3
X2
X1
X0
P3
P2
P1
P0
I1
H3
G4
F4
I2
H4
G5
F5
Add-3
Ckt
X3
X2
X1
X0
P3
P2
P1
P0
E3
D2
C1
B
E4
D3
C2
B1

## Slide 12: BCD
Output= H4 G5 F5 E4 D3 C2 B1 A
( from previous slide)
Name the final output of BCD as
    Output = U3U2U1U0 L3L2L1L0
Use I2 as Overflow.
Add-3
Ckt
X3
X2
X1
X0
P3
P2
P1
P0
0
H
G
F
I
H1
G1
F1
Add-3
Ckt
X3
X2
X1
X0
P3
P2
P1
P0
H1
G1
F1
E
H2
G2
F2
E1
Add-3
Ckt
X3
X2
X1
X0
P3
P2
P1
P0
G2
F2
E1
D
G3
F3
E2
D1
Add-3
Ckt
X3
X2
X1
X0
P3
P2
P1
P0
0
I
H2
G3
J
I1
H3
G4
Add-3
Ckt
X3
X2
X1
X0
P3
P2
P1
P0
F3
E2
D1
C
F4
E3
D2
C1
Add-3
Ckt
X3
X2
X1
X0
P3
P2
P1
P0
I1
H3
G4
F4
Overflow
U3
U2
U1
Add-3
Ckt
X3
X2
X1
X0
P3
P2
P1
P0
E3
D2
C1
B
U0
L3
L2
L1
A = L0.

## Slide 13: BCD Block Diagram
BCD Block Diagram
A
B
C
D
E
F
G
H
U0
U1
U2
U3
L0
L1
L2
L3
Implement the BCD Ckt from previous slide.
Simulate the ckt (screen shots for report.)
Create a block symbol (bsf) file for BCD circuit.
    Creating a symbol block
Overflow

## Slide 14: Example
 |  | BCD |  |  |  |  |  |  |  | Binary |  |  |  |  |  |  | 
 | OF | U3U2U1U0 |  |  |  | L3L2L1L0 |  |  |  |  |  |  |  |  |  |  | 
 |  | 2^3 | 2^2 | 2^1 | 2^0 | 2^3 | 2^2 | 2^1 | 2^0 | 0 | 1 | 1 | 0 | 0 | 0 | 1 | 1
Shift 1 |  | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 1 | 0 | 0 | 0 | 1 | 1 | 
Shift 2 |  | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 1 | 0 | 0 | 0 | 1 | 1 |  | 
Shift 3 |  | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 1 | 0 | 0 | 0 | 1 | 1 |  |  | 
Shift 4 |  | 0 | 0 | 0 | 0 | 0 | 1 | 1 | 0 | 0 | 0 | 1 | 1 |  |  |  | 
Add- 3 |  |  |  |  |  | 0 | 0 | 1 | 1 |  |  |  |  |  |  |  | 
 |  | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 1 | 0 | 0 | 1 | 1 |  |  |  | 
Shift 5 |  | 0 | 0 | 0 | 1 | 0 | 0 | 1 | 0 | 0 | 1 | 1 |  |  |  |  | 
Shift 6 |  | 0 | 0 | 1 | 0 | 0 | 1 | 0 | 0 | 1 | 1 |  |  |  |  |  | 
Shift 7 |  | 0 | 1 | 0 | 0 | 1 | 0 | 0 | 1 | 1 |  |  |  |  |  |  | 
Add 3 |  |  |  |  |  | 0 | 0 | 1 | 1 |  |  |  |  |  |  |  | 
 |  | 0 | 1 | 0 | 0 | 1 | 1 | 0 | 0 | 1 |  |  |  |  |  |  | 
Shift 8 |  | 1 | 0 | 0 | 1 | 1 | 0 | 0 | 1 |  |  |  |  |  |  |  | 
9
9

## Slide 15: Example
 |  | BCD |  |  |  |  |  |  |  | Binary |  |  |  |  |  |  | 
 | OF | U3U2U1U0 |  |  |  | L3L2L1L0 |  |  |  |  |  |  |  |  |  |  | 
 |  | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 1 | 0 | 0 | 1 | 0 | 0
Shift 1 |  | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 1 | 0 | 0 | 1 | 0 | 0 | 
Shift 2 |  | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 1 | 0 | 0 | 1 | 0 | 0 |  | 
Shift 3 |  | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 1 | 0 | 0 | 1 | 0 | 0 |  |  | 
Shift 4 |  | 0 | 0 | 0 | 0 | 0 | 1 | 1 | 0 | 0 | 1 | 0 | 0 |  |  |  | 
Add- 3 |  |  |  |  |  | 0 | 0 | 1 | 1 |  |  |  |  |  |  |  | 
 |  | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 1 | 0 | 1 | 0 | 0 |  |  |  | 
Shift 5 |  | 0 | 0 | 0 | 1 | 0 | 0 | 1 | 0 | 1 | 0 | 0 |  |  |  |  | 
Shift 6 |  | 0 | 0 | 1 | 0 | 0 | 1 | 0 | 1 | 0 | 0 |  |  |  |  |  | 
Add 3 |  |  |  |  |  | 0 | 0 | 1 | 1 |  |  |  |  |  |  |  | 
 |  | 0 | 0 | 1 | 0 | 1 | 0 | 0 | 0 | 0 | 0 |  |  |  |  |  | 
Shift 7 |  | 0 | 1 | 0 | 1 | 0 | 0 | 0 | 0 |  |  |  |  |  |  |  | 
 |  | 0 | 0 | 1 | 1 |  |  |  |  |  |  |  |  |  |  |  | 
 |  | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 |  |  |  |  |  |  |  | 
Shift 8 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 |  |  |  |  |  |  |  |  | 
and OF = 1 (overflow)

## Slide 16
 |  | BCD |  |  |  |  |  |  |  | Binary |  |  |  |  |  |  | 
 | OF | U3U2U1U0 |  |  |  | L3L2L1L0 |  |  |  |  |  |  |  |  |  |  | 
 |  | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | H | G | F | E | D | C | B | A
Shift 1 |  | 0 | 0 | 0 | 0 | 0 | 0 | 0 | H | G | F | E | D | C | B | A | 
Shift 2 |  | 0 | 0 | 0 | 0 | 0 | 0 | H | G | F | E | D | C | B | A |  | 
Shift 3 |  | 0 | 0 | 0 | 0 | 0 | H | G | F | E | D | C | B | A |  |  | 
 |  | If 0HGF > 4, I H1 G1 F1= 0HGF + 0011 |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
 |  | 0 | 0 | 0 | 0 | I | H1 | G1 | F1 | E | D | C | B | A |  |  | 
Shift 4 |  | 0 | 0 | 0 | I | H1 | G1 | F1 | E | D | C | B | A |  |  |  | 
 |  | If H1 G1 F1 E > 4, H2 G2 F2 E1 = H1 G1 F1 E + 0011 |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
 |  | 0 | 0 | 0 | I | H2 | G2 | F2 | E1 | D | C | B | A |  |  |  | 
Shift 5 |  | 0 | 0 | I | H2 | G2 | F2 | E1 | D | C | B | A |  |  |  |  | 
 |  | If G2 F2 E1 D> 4, G3 F3 E2 D1= G2 F2 E1 D + 0011 |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
 |  | 0 | 0 | I | H2 | G3 | G3 | E2 | D1 | C | B | A |  |  |  |  | 
Shift 6 |  | 0 | I | H2 | G3 | F3 | E2 | D1 | C | B | A |  |  |  |  |  | 
 |  | If I H2 G3 > 4, J I1 H3 G4 =I H2 G3 + 0011 If F3 E2 D1 C> 4, F4 E3 D3 C1= F3 E3 D1 C+ 0011 |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
 |  | J | I1 | H3 | G4 | F4 | E3 | D2 | C1 | B | A |  |  |  |  |  | 
Shift 7 |  | I1 | H3 | G4 | F4 | E3 | D2 | C1 | B | A |  |  |  |  |  |  | 
 |  | If I1 H3 G4 F4 > 4, I2 H4 G5 F5 = I1 H3 G4 F4 + 0011 If E3 D2 C1 B > 4, E4 D3 C2 B1 = E3 D2 C1 B + 0011 |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
 |  | I2 | H4 | G5 | F5 | E4 | D3 | C2 | B1 | A |  |  |  |  |  |  | 
Shift 8 | I2 | H4 | G5 | F5 | E4 | D3 | C2 | B1 | A |  |  |  |  |  |  |  | 

## Slide 17: BCD Circuit with 7 Segment Display
BCD Ckt
Display
ckt
Display
ckt
X0
X1
X2
x3
X0
X1
X2
x3
U0
U1
U2
U3
L0
L1
L2
L3
A
B
C
D
E
F
G
H
0001 1001 (25 in Decimal)
0010 (2 for tens Display)
0101 (5 for units Display)
Overflow
D0
D1
D2
D3
D4
D5
D6
D0
D1
D2
D3
D4
D5
D6
D00
D01
D02
D03
D04
D05
D06
D10
D11
D12
D13
D14
D15
D16
Create a block symbol (bsf) file for the display circuit (Lab 2).
Combine BCD and display circuit as below.
Create a block symbol (bsf) file for the combined circuit.

## Slide 18: BCD Top Level
BCD
Top Level
A
B
C
D
E
F
G
H
Toggle Switch
Hex1
Hex0
D00
D01
D02
D03
D04
D05
D06
D10
D11
D12
D13
D14
D15
D16
Overflow assigns to one of the LEDs.
Download the final top-level circuit to DE2 Board.

## Slide 19: Extra Credits
Modify your BCD circuit such that it can display up to 199 using three 7 segment display. (10 points.)

## Slide 20: Assignment Flow Chart for BCD and Display Ckt
Implement ADD-3 Ckt and Create the Block Symbol
Implement BCD Ckt
Combine the BCD and Display Ckt
Simulation Waveform
Pin Assignment
Downloading to DE 1 Board

## Slide 21: Creating a symbol block
Display Ckt
We can reuse the previous ckt by creating a block symbol instead of inserting the whole ckt.
we can create the existing ckt to a symbol block and adding in other project as a block.

## Slide 22: Creating a symbol block
File -> Create/Update -> Create Symbol Files for current file
save the symbol file in your project folder. This will create a .bsf file.

## Slide 23: Adding Existing Ckt as a symbol to new project.
Create a new Schematic Block file and Open Symbol window from Right Click-> Insert -> Symbol.
1.
2. Select the desired .bsf file and add it the same way as you add other digital circuit components.