## Slide 1: Lab 5-A
Counter and 8 Bit Register
  i. Counter
    Design a 3 Bit Up Counter with Reset.
  ii. 8 Bit Register
    Design a 8 Bit Register which stores and outputs a 8 bit binary input on clock rising edge with ‘Low’ on Load Input.

## Slide 2: Counter Design Example
Design a 3 bit up counter which counts 0,1,2,3,4.
Invalid states should go to 0
Hold at 4
0
1
4

## Slide 3: Counter Design Example
1. Complete the truth table for 3 bit up counter.
2. Find the Boolean expression for .
3. I.
PS | NS

## Slide 4: Counter Block Diagram
DFF A
DFF B
DFF C
Combinational Ckt
Input
From Flip Flip
Output
Output
Output
Give VCC to PRN.
Clock Input
Connect to the CLR of DFF.
In Quartus prime dff is a D flip-flop with a rising-edge trigger.

## Slide 5: Simulate 3 Bit Counter Circuit
Run the 3 bit counter simulation.
Hint: when reset is zero the counter will reset.

## Slide 6: A 8 bit Register Using Dff
A register is a storage or memory component in a digital ckt.
If (clock rising edge and LOAD = ‘0’)
  Output = input;
Else
  Output = Prev_Output;
End if;
clk
LOAD
Input
Output
5
5
8
13
5
6
8
8
8

## Slide 7: Register using D Flip Flop
D FF
Din
Clk
Q
D | Clk | Q+
x | 0 | No change
1 | Rising Edge | 1
0 | Rising Edge | 0

## Slide 8: Modified D Flip Flop
Modify D FF with an extra input: Load.
D FF
Din
Clk
Q
D | Clk | LOAD | Q+
x | 0 | 1 | No change
x | Rising Edge | 1 | No Change
1 | Rising Edge | 0 | 1
0 | Rising Edge | 0 | 0
Load
Clk
D
And
1
0
0

## Slide 9: Modified D Flip Flop
Modify D FF with an extra input: Load.
D FF
Din
Clk
Q
D | Clk | LOAD | Q+
x | 0 | 1 | No change
x | Rising Edge | 1 | No Change
1 | Rising Edge | 0 | 1
0 | Rising Edge | 0 | 0
Load
Clk
D
And
0
1

## Slide 10: 8 Bit Register
Give VCC to PRN.
FFA
FFB
FFH
.
.
.
.
.
.
A
QA
H
QH
D
clk
B
Load Input
Clock Input
QB
Reset Input connect
to all CLR pin of FF.
Reset Input
AND
AND
AND

## Slide 11: Register Block Diagram
8 Bit Register
Data Inputs
LOAD Input
Clock Input
Data Outputs
A
B
C
D
E
F
G
H
QA
QB
QC
QD
QE
QF
QG
QH
Reset

## Slide 12: Simulate the 8 Bit Register
Hint: when reset is zero the register is clear.
when load ==0 and clock rising edge
Output = Current Input
when load ==1
output = Previous Input.

## Slide 13: Simulation and Downloading
Simulation Waveform for Counter and 8 bit Register.
Download Counter Ckt to DE1 Board.